## Slide 1: LFAB Vendor/Supplier Safety Meeting
01/21/2025

## Slide 2: Safety Culture - Marja
Human knowledge, belief, and behavior
Shared attitudes, values, goals, and practices
Characteristic features of everyday existence shared by people
We Define our Safety Culture
What creates a culture?

## Slide 3: LFAB Injury Metrics WW02 - Marja
Entire Site
Contract Employees
No WW02 Injuries

## Slide 4: Lifting Requirements- Tori
At LFAB, we have a 40 lb max lifting limit
  This means no matter what, employees are never to lift over 40 lbs without assistance
  This limit is for “ideal lifts” only
    Ideal lifts = perfectly ergonomic lifts
There are other factors involved with lifting that may reduce the allowable lifting limit well below 40 lbs, these make a lift “less than ideal”
These factors include, but are not limited to:
  Extending arms from main frame of body
  Twisting
  Overhead lifts
  Lifting while bent forward
  Poor grip/hand holds
  Repetition of lifts
  Carrying or extended hold of object
  Lifting with back or arms instead of legs
  Restricted lifting space
  Poor footing
  Limiting personal factors
Acceptable lifts
Less than 40lbs & Ideal posture
Less than 80lbs, evenly distributed weight & Ideal posture
Anytime a lift-assist is available and is an acceptable option, please use

## Slide 5: OEM Expectations QRC – Justin Furey

## Slide 6: Project Kick off Safety Meeting (Install/Deinstall/Conversion)
Attendee’s
  SM/EM
  EOs
  Suppliers
  Techs
  Safety Rep
Vendors Safety Walk – Project Area
  Emergency Exits
  Cover Strobes (fire, TGMS)
  Eye Wash Shower locations
  Ensure only approved cutting devices are brought into the fab
  Cover clean room approved materials
  Required PPE
    Use of cut resistant gloves, bump caps, safety glasses, steel toe shoes
  Nearest PPE location
  House cleaning expectations – 5S, barricades labeled
Cover Equipment Safe States
  All panels on and doors closed when equipment is not being worked on
    If panels cannot be installed barricade is placed around the tool with a label
  LOTO Devices installed when appropriate
  Show team where the laydown area is located and ensure it is barricaded/labeled
  Chemistries/Gases
  Highlight other activities that are happening in and around the area
Specific Risks for Project
  Highlight any other risks for the specific project

## Slide 7: Safe Collaboration at LFAB
LFAB has many individuals and companies partnering daily to accomplish key projects and tasks
Construction activities will continue at this site for years to come
We must avoid the ambiguity of “gray zones” between teams
“Gray zones” create unknown or unclear conditions and increase risk to safe execution
What can we do?
When executing procedures, PTPs, etc:
  Define the specific responsibilities for each team
  Identify the critical handoff points and verify the receiving team has full understanding
Do not jump in to help tasks outside your scope
  You may not have the necessary training, background/details, or equipment to safely perform the task
  Stop work and escalate to your leadership team if you are not getting response from the responsible party
PAUSE
Effective communication and collaboration will help support the safety of all LFAB site workers
Plan
Plan
Plan

## Slide 8: Safety Sharing
Frank Young Construction – Bill Tibbett

## Slide 9
Flooring Risks at LFAB

## Slide 10
Shout-outs
Spectrum West – Trevor Emery, was working in 50 Sub Fab and was having trouble finding safe access to a manifold. He reached out to me to collaborate and after looking at the area we determined that scaffolding would be the only way to safely access the manifold tie in.
Rocky Mountain Specialty Contractor – Thank you to Gonzalo Navarro and David Quiros for meeting with Spectum and coming up with a plan to install a ladder and platform for safe access.

## Slide 11
Shout-outs
Ulvac – Alec Turner reached out to me after a TI Audit and wanted to confirm his PVD team was in compliance with site safety protocols.
Brad Dalrymple confirmed the Vendors have a specific process for Tool Install and safety.
Brad is managing these Vendors
PVD – AMAT, Ulvac
Implant – AMAT, Axcelis
RTP – AMAT, Veeco, LaserMark

## Slide 12
Q & A